To:	Users
From:	The Author
Subj:	Simulator Usage, V2.2
Date:	27-Jan-96

This memorandum documents the PDP-8, PDP-11, PDP 18b, and Nova simulators.
These simulators are freeware; commercial use is prohibited, and support is
not available.  The best way to fix problems or add features is to read
and modify the sources yourself.  Alternately, you can send Internet mail
to dsmaint@pa.dec.com; but responses are NOT guaranteed.

The simulators use a common command interface.  The memorandum first
describes the common features of the command interface and then provides
information on each of the individual simulators.


1. Compiling And Running A Simulator

The simulators have been tested on VAX VMS, Alpha VMS, Alpha UNIX,
and Intel LINUX.  Porting to other environments will require changes
to the operating system dependent code in scp_tty.c.

To compile the simulators on Alpha UNIX, use these commands (note that
separate compilations are required for each of the 18b PDP's):

	% cc pdp8*.c scp*.c -lm -o pdp8
	% cc pdp11*.c scp*.c -o pdp11
	% cc nova*.c scp*.c -lm -o nova
	% cc -DPDP{4,7,9,15} pdp18b*.c scp*.c -lm -o pdp{4,7,9,15}

To compile the simulators on LINUX, use these commands:

	% cc -DLINUX pdp8*.c scp*.c -lm -lbsd -o pdp8
	% cc -DLINUX pdp11*.c scp*.c -lbsd -o pdp11
	% cc -DLINUX nova*.c scp*.c -lm -lbsd -o nova
	% cc -DPDP{4,7,9,15} -DLINUX pdp18b*.c scp*.c -lm -o pdp{4,7,9,15}

To start the simulator, simply type its name.  The simulator takes
one optional argument, a startup command file.  If specified, this
file should contain a series of non-interactive simulator commands,
one per line.  These command can be used to set up standard parameters,
for example, disk sizes.

	% pdp8 <startup file>(cr)		or
	% pdp11 <startup file>(cr)		or
	% nova <startup file>(cr)		or
	% pdp{4,7,9,15} <startup file>(cr)

The simulator types out its name and version, executes the commands
in the startup file, if any, and then prompts for input with

	sim>


2. Simulator Conventions

A simulator consists of a series of devices, the first of which is always
the CPU.  A device consists of named registers and one or more numbered
units.  Registers correspond to device state, units to device address
spaces.  Thus, the CPU device might have registers like PC, ION, etc,
and a unit corresponding to main memory; a disk device might have
registers like BUSY, DONE, etc, and units corresponding to individual
disk drives.  Except for main memory, device address spaces are simulated
as unstructured binary disk files in the host file system.  (Thus, files
with data widths greater than 8b are endian dependent.)  The SHOW CONFIG
command displays the simulator configuration.

A simulator keeps time in terms of arbitrary units, usually one time unit
per instruction executed.  Simulated events (such as completion of I/O)
are scheduled at some number of time units in the future.  The simulator
executes synchronously, invoking event processors when simulated events
are scheduled to occur.  Even asynchronous events, like keyboard input,
are handled by polling at synchronous intervals.  The SHOW QUEUE command
displays the simulator event queue.


3. Commands

3.1 Loading Programs

The LOAD command (abbreviation LO) loads a file in binary paper-tape
loader format:

	sim> load <filename>(cr)

3.2 Saving and Restoring State

The SAVE command (abbreviation SA) save the complete state of the
simulator to a file.  This includes the contents of main memory and
all registers, and the I/O connections of devices:

	sim> save <filename>(cr)

The RESTORE command (abbreviation REST, alternately GET) restores a
previously saved simulator state:

	sim> restore <filename>(cr)

Note: SAVE file format compresses zeroes to minimize file size.

3.3 Resetting Devices

The RESET command (abbreviation RE) resets a device or the entire
simulator to a predefined condition:

	sim> RESET(cr)			-- reset all devices
	sim> RESET ALL(cr)		-- reset all devices
	sim> RESET <device>(cr)		-- reset specified device

Typically, RESET stops any in-progress I/O operation, clears any
interrupt request, and returns the device to a quiescent state.  It
does not clear main memory or affect I/O connections.

3.4 Connecting and Disconnecting Devices

Except for main memory, simulated unit address spaces are simulated as
unstructured binary disk files in the host file file system.  Before using
a simulated unit the user must specify the file to be used by a particular
unit.  The ATTACH (abbreviation AT) command associates a unit and a file:

	sim> ATTACH <device><unit number> <filename>(cr)

If the file does not exist, it is created, and an appropriate message
is printed.

The DETACH (abbreviation DET) command breaks the association between a
unit and a file and closes the file:

	sim> DETACH ALL(cr)			-- detach all units
	sim> DETACH <device><unit number>(cr)	-- detach specified unit

The EXIT command performs an automatic DETACH ALL.

3.5 Examining and Changing State

There are four commands to examine and change state:

	EXAMINE (abbreviated E) examines state
	DEPOSIT (abbreviated D) changes state
	IEXAMINE (interactive examine, abbreviated IE) examines state
		and allows the user to interactively change it
	IDEPOSIT (interactive deposit, abbreviated ID) allows the user
		to interactively change state

All four commands take the form

	command {-switches} {<device>{<unit number>}} <state list>

Deposit must also include a deposit value at the end of the command.

The examine and deposit commands can work on the address space of any
unit.  If no device is specified, the CPU (main memory) is selected; if
a device but no unit is specified, unit 0 of the specified device is
selected.  The "state list" consists of one or more of the following,
separated by commas:

	register		the specified register
	register1-register2	all the registers starting at register1
				up to and including register2
	address			the specified location
	address1-address2	all locations starting at address1 up to
				and including address2
	STATE			all registers in the device
	ALL			all locations in the unit

Switches can be used to control the format of display information:

	-a			display as ASCII
	-c			display as character string
	-m			display as instruction mnemonics

The simulators typically accept symbolic input (see simulator sections).

Examples:

	sim> ex 1000-1100		-- examine 1100:1100
	sim> de PC 1040			-- set PC to 1040
	sim> ie 40-50			-- interactively examine 40:50
	sim> ex rx0 50060		-- examine 50060, RX unit 0
	sim> de all 0			-- set main memory to 0

Note: to terminate an interactive command, simply type a bad value (eg,
XXX) when input is requested.

3.6 Running Programs

The RUN command (abbreviated RU) resets all devices, deposits its argument
(if given) in the PC, and starts execution.  If no argument is given,
execution starts at the current PC.

The GO command does NOT reset devices, deposits its argument (if given) in
the PC, and starts execution.  If no argument is given, execution starts at
the current PC.

The CONT command (abbreviated CO) does NOT reset devices and resumes
execution at the current PC.

The STEP command (abbreviated S) resumes execution at the current PC for
the number of instructions given by its argument.  If no argument is
supplied, one instruction is executed.

The BOOT command (abbreviated BO) bootstraps the device and unit given
by its argument.  If no unit is supplied, unit 0 is boostrapped.  The
specified unit must be attached to a file.

3.7 Stopping Programs

Programs run until the simulator detects an error or stop condition, or
until the user forces a stop condition.

3.7.1 Simulator Detected Stop Conditions

These simulator-detected conditions stop simulation:

o HALT instruction.  If a HALT instruction is decoded, simulation stops.

o Breakpoint.  The IBKPT register provides a single virtual address
  breakpoint.  If the PC matches the contents of the IBKPT register,
  simulation stops.  The breakpoint is automatically disabled for
  the next instruction execution.

o I/O error.  If an I/O error occurs during simulation of an I/O operation,
  and the device stop-on-I/O-error flag is set, simulation usually stops.

o Processor condition.  Certain processor conditions can stop simulation;
  these are described with the individual simulators.

3.7.2 User Specified Stop Conditions

Typing the interrupt character stops simulation.  The interrupt character
is defined by the WRU (where are you) register and is initially set to
005 (^E).

3.8 Setting Device Parameters

The SET command (abbreviated SE) changes the status of a device parameter:

	sim> SET <unit> <parameter>

The parameters are simulator and device specific.  Disk drives, for
example, can usually be set write ENABLED or write LOCKED; if a device
supports multiple drive types, the SET command can be used to specify
the drive type.

3.8 Displaying Parameters and Status

The SHOW CONFIGURATION command shows the simulator configuration and the
status of all simulated I/O devices.

The SHOW <device> command shows the status of the named simulated I/O
device.

The SHOW QUEUE command shows the state of the simulator event queue.  Times
are in "simulation units", typically one unit per instruction execution,
relative to the current simulation time.

The SHOW TIME command shows the number of time units elapsed since
the last RUN command.

3.9 Exiting The Simulator

EXIT (synonyms QUIT and BYE) returns control to the operating system.


4. PDP-8 Features

The PDP-8 simulator is configured as follows:

device		simulates
name(s)

CPU		PDP-8/E CPU with 32KW of memory
-		KE8E extended arithmetic element (EAE)
-		KM8E memory management and timeshare control
PTR,PTP		PC8E paper tape reader/punch
TTI,TTO		KL8E console terminal
LPT		LE8E line printer
CLK		DK8E line frequency clock (also PDP-8/A compatible)
RK		RK8E/RK05 cartridge disk controller with four drives
RF		RF08/RS08 fixed head disk controller with four platters
RX		RX8E/RX01 floppy disk controller with two drives
MT		TM8E/TU10 magnetic tape controller with eight drives

The PDP-8 simulator implements one unique stop condition: if an undefined
instruction (unimplemented IOT or OPR) is decoded, and register STOP_INST
is set, the simulator halts.

4.1 CPU

The only CPU options are the presense of the EAE and the size of main memory;
the memory extension and time-share control is always included, even if
memory size is 4K.

	SET CPU EAE		enable EAE
	SET CPU NOEAE		disable EAE
	SET CPU 4K		set memory size = 4K
	SET CPU 8K		set memory size = 8K
	SET CPU 12K		set memory size = 12K
	SET CPU 16K		set memory size = 16K
	SET CPU 20K		set memory size = 20K
	SET CPU 24K		set memory size = 24K
	SET CPU 28K		set memory size = 28K
	SET CPU 32K		set memory size = 32K

If memory size is being reduced, and the memory being truncated contains
non-zero data, the simulator asks for confirmation.  Data in the truncated
portion of memory is lost.  Initial memory size is 32K.

CPU registers include the visible state of the processor as well as the
control registers for the interrupt system.

	name		size	comments

	PC		15	program counter, including IF as high 3 bits
	AC		12	accumulator
	MQ		12	multiplier-quotient
	L		1	link
	SR		12	front panel switches
	IF		3	instruction field
	DF		3	data field
	IB		3	instruction field buffer
	SF		7	save field
	UF		1	user mode flag
	UB		1	user mode buffer
	SC		5	EAE shift counter
	GTF		1	EAE greater than flag
	EMODE		1	EAE mode (0 = A, 1 = B)
	ION		1	interrupt enable
	ION_DELAY	1	interrupt enable delay for ION
	CIF_DELAY	1	interrupt enable delay for CIF
	PWR_INT		1	power fail interrupt
	UF_INT		1	user mode violation interrupt
	INT		15	interrupt pending flags
	DONE		15	device done flags
	ENABLE		15	device interrupt enable flags
	OLDPC		15	PC prior to last JMP, JMS, or interrupt
	STOP_INST	1	stop on undefined instruction
	BREAK		16	breakpoint address (177777 to disable)
	WRU		8	interrupt character

4.2 Programmed I/O Devices (PTR, PTP, TTI, TTO, CLK, LPT)

The paper tape reader (PTR), paper tape punch (PTP), and line printer
(LPT) read data from or write data to disk files.  The POS register
specifies the number of the next data item to be read or written.  Thus,
by changing POS, the user can backspace or advance these devices.

The programmed I/O devices typically implement these registers:

	name		size	comments

	BUF		8	last data item processed
	INT		1	interrupt pending flag
	DONE		1	device done flag
	ENABLE		1	interrupt enable flag
	TIME		24	time from I/O initiation to interrupt
				(for keyboard, polling interval)
	POS		32	position in the input or output file
	STOP_IOE	1	stop on I/O error

For the serial devices, error handling is as follows:

	type	error	     STOP_IOE	processed as

	in,out	not attached	1	report error and stop
				0	out of tape or paper

	in	end of file	1	report error and stop
				0	out of tape or paper

	in,out	OS I/O error	x	report error and stop

4.3 RK8E/RK05

RK8E options include the ability to place units online or offline,
write enabled or write locked:

	SET RKn OFFLINE		set unit n offline
	SET RKn ONLINE		set unit n online
	SET RKn LOCKED		set unit n write locked
	SET RKn ENABLED		set unit n write enabled

The RK8E implements these registers:

	name		size	comments

	STA		12	status
	DA		12	disk address
	MA		12	current memory address
	CMD		12	disk command
	BUSY		1	control busy flag
	INT		1	interrupt pending flag
	STIME		24	seek time, per cylinder
	RTIME		24	rotational delay
	STOP_IOE	1	stop on I/O error

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

	end of file	x	assume rest of disk is zero

	OS I/O error	x	report error and stop

4.4 RX8E/RX01

RX8E options include the ability to set units write enabled or write locked:

	SET RXn LOCKED		set unit n write locked
	SET RXn ENABLED		set unit n write enabled

The RX8E implements these registers:

	name		size	comments

	RXCS		12	status
	RXDB		12	data buffer
	RXES		8	error status
	RXTA		8	current track
	RXSA		8	current sector
	STAPTR		3	controller state
	BUFPTR		3	buffer pointer
	INT		1	interrupt pending flag
	DONE		1	device done flag
	ENABLE		1	interrupt enable flag
	TR		1	transfer ready flag
	ERR		1	error flag
	CTIME		24	command completion time
	STIME		24	seek time, per track
	XTIME		24	transfer ready delay
	STOP_IOE	1	stop on I/O error

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

RX01 data files are buffered in memory; therefore, end of file and OS
I/O errors cannot occur.

4.5 RF08/RS08

The RF08 implements these registers:

	name		size	comments

	STA		12	status
	DA		20	current disk address
	MA		12	memory address (in memory)
	WC		12	word count (in memory)
	WLK		32	write lock switches
	INT		1	interrupt pending flag
	DONE		1	device done flag
	TIME		24	rotational delay, per word
	BURST		1	burst flag
	STOP_IOE	1	stop on I/O error

The RF08 is a three-cycle data break device.  If BURST = 0, word transfers
are scheduled individually; if BURST = 1, the entire transfer occurs in
a single data break.

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

RF08 data files are buffered in memory; therefore, end of file and OS
I/O errors cannot occur.

4.6 Magnetic Tape (MT)

Magnetic tape options include the ability to place units write enabled or
or write locked.

	SET MTn LOCKED		set unit n write locked
	SET MTn ENABLED		set unit n write enabled

The magnetic tape controller implements these registers:

	name		size	comments

	CMD		12	command
	FNC		12	function
	CA		12	memory address
	WC		12	word count
	DB		12	data buffer
	STA		12	main status
	STA2		6	secondary status
	DONE		1	device done flag
	INT		1	interrupt pending flag
	STOP_IOE	1	stop on I/O error
	TIME		24	record delay
	UST0..7		24	unit status, units 0..n

Error handling is as follows:

	error		processed as

	not attached	tape not ready

	end of file	(read or space) end of physical tape
			(write) ignored

	OS I/O error	report error and stop

4.7 Symbolic Display and Input

The PDP-8 simulator implements symbolic display and input.  Display is
controlled by command line switches:

	-a			display as ASCII character
	-c			display as (sixbit) character string
	-m			display instruction mnemonics

Input parsing is controlled by the first character typed in:

	'			ASCII character
	"			two character sixbit string
	alphabetic		instruction mnemonic
	numeric			octal number

Instruction input uses standard PDP-8 assembler syntax.  There are four
instruction classes: memory reference, IOT, field change, and operate.

Memory reference instructions have the format

	memref {I} {T/Z} address

where I signifies indirect, T a current page reference, and Z a zero page
reference.  The address is an octal number in the range 0 - 07777; if T or
Z is specified, the address is a page offset in the range 0 - 177.  Normally,
T is not needed; the simulator figures out from the address what mode to use.
However, when referencing memory outside the CPU (eg, disks), there is no
valid PC, and T must be used to specify current page addressing.

IOT instructions consist of single mnemonics, eg, KRB, TLS.  IOT instructions
may be or'd together

	iot iot iot...

The simulator does not check the legality of the proposed combination.  IOT's
for which there is no opcode may be specified as IOT n, where n is an octal
number in the range 0 - 0777.

Field change instructions (CIF, CDF) have the format

	fldchg field

where field is an octal number in the range 0 - 7.  Field change instructions
may be or'd together.

Operate instructions have the format

	opr opr opr...

The simulator does not check the legality of the proposed combination.  EAE
mode A and B mnemonics may be specified regardless of the EAE mode.  The
operands for MUY and DVI must be deposited explicitly.


5. PDP-11 Features

The PDP-11 simulator is configured as follows:

device		simulates
name(s)

CPU		J-11 CPU with 256KB of memory
-		FP11 floating point unit (FPA)
PTR,PTP		PC11 paper tape reader/punch
TTI,TTO		DL11 console terminal
LPT		LP11 line printer
CLK		line frequency clock
RK		RK11/RK05 cartridge disk controller with eight drives
RL		RLV12/RL01(2) cartridge disk controller with four drives
RX		RX11/RX01 floppy disk controller with two drives

The PDP-11 simulator implements several unique stop conditions:

	- abort during exception vector fetch, and register STOP_VEC is set
	- abort during exception stack push, and register STOP_SPA is set
	- trap condition 'n' occurs, and register STOP_TRAP<n> is set
	- wait state entered, and no I/O operations outstanding
	  (ie, no interrupt can ever occur)

5.1 CPU

Memory size is a compile time parameter in pdp11_defs.h; the standard
memory size is 248KB.

These switches are recognized when examining or depositing in CPU memory:

	-v			interpret address as virtual
	-d			if mem mgt enabled, force data space
	-k			if mem mgt enabled, force kernel mode
	-s			if mem mgt enabled, force supervisor mode
	-u			if mem mgt enabled, force user mode
	-p			if mem mgt enabled, force previous mode

CPU registers include the visible state of the processor as well as the
control registers for the interrupt system.

	name		size	comments

	PC		16	program counter
	R0..R5		16	R0..R5, first register set
	R10..R15	16	R0..R5, second register set
	KSP		16	kernel stack pointer
	SSP		16	supervisor stack pointer
	USP		16	user stack pointer
	PSW		16	processor status word
	  CM		2	  current mode, PSW<15:14>
	  PM		2	  previous mode, PSW<13:12>
	  RS		2	  register set, PSW<11>
	  IPL		3	  interrupt priority level, PSW<7:5>
	  T		1	  trace bit, PSW<4>
	  N		1	  negative flag, PSW<3>
	  Z		1	  zero flag, PSW<2>
	  V		1	  overflow flag, PSW<1>
	  C		1	  carry flag, PSW<0>
	SR		16	front panel switches
	DR		16	front panel display
	MEMERR		16	memory error register
	CCR		16	cache control register
	MAINT		16	maintenance register
	HITMISS		16	hit/miss register
	CPUERR		16	CPU error register
	PIRQ		16	programmed interrupt requests
	FAC0H..FAC5H	32	FAC0..FAC5, high 32 bits
	FAC0L..FAC5L	32	FAC0..FAC5, low 32 bits
	FPS		16	floating point status
	FEA		16	floating exception address
	FEC		4	floating exception code
	MMR0..3		16	memory management registers 0..3
	{K/S/U}{I/D}{PAR/PDR}{0..7}
			16	memory management registers
	INT		32	interrupt pending flags
	TRAP		18	trap pending flags
	WAIT		0	wait state flag
	WAIT_ENABLE	0	wait state enable flag
	STOP_TRAPS	18	stop on trap flags
	STOP_VECA	1	stop on read abort in trap or interrupt
	STOP_SPA	1	stop on stack push abort in trap or interrupt
	OLDPC		16	PC prior to last JMP, JMS, or interrupt
	BREAK		16	breakpoint address (1 to disable)
	WRU		8	interrupt character

5.2 Programmed I/O Devices (PTR, PTP, TTI, TTO, CLK, LPT)

The paper tape reader (PTR), paper tape punch (PTP), and line printer
(LPT) read data from or write data to disk files.  The POS register
specifies the number of the next data item to be read or written.  Thus,
by changing POS, the user can backspace or advance these devices.

The programmed I/O devices typically implement these registers:

	name		size	comments

	BUF		8	last data item processed
	CSR		16	control/status register
	INT		1	interrupt pending flag
	ERR		1	error flag (CSR<15>)
	DONE		1	device done flag (CSR<7>)
	IE		1	interrupt enable flag (CSR<6>)
	TIME		24	time from I/O initiation to interrupt
				(for keyboard, polling interval)
	POS		32	position in the input or output file
	STOP_IOE	1	stop on I/O error

For the serial devices, error handling is as follows:

	type	error	     STOP_IOE	processed as

	in,out	not attached	1	report error and stop
				0	out of tape or paper

	in	end of file	1	report error and stop
				0	out of tape or paper

	in,out	OS I/O error	x	report error and stop

5.3 RK11/RK05

RK11 options include the ability to place units online or offline,
write enabled or write locked:

	SET RKn OFFLINE		set unit n offline
	SET RKn ONLINE		set unit n online
	SET RKn LOCKED		set unit n write locked
	SET RKn ENABLED		set unit n write enabled

The RK11 implements these registers:

	name		size	comments

	RKCS		16	control/status
	RKDA		16	disk address
	RKBA		16	memory address
	RKWC		16	word count
	RKDS		16	drive status
	RKER		16	error status
	INTQ		9	interrupt queue
	DRVN		3	number of last selected drive
	INT		1	interrupt pending flag
	ERR		1	error flag (CSR<15>)
	DONE		1	device done flag (CSR<7>)
	IE		1	interrupt enable flag (CSR<6>)
	INT		1	interrupt pending flag
	STIME		24	seek time, per cylinder
	RTIME		24	rotational delay
	STOP_IOE	1	stop on I/O error

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

	end of file	x	assume rest of disk is zero

	OS I/O error	x	report error and stop

5.4 RX11/RX01

RX11 options include the ability to make units write enabled or write locked:

	SET RXn LOCKED		set unit n write locked
	SET RXn ENABLED		set unit n write enabled

The RX11 implements these registers:

	name		size	comments

	RXCS		12	status
	RXDB		8	data buffer
	RXES		8	error status
	RXERR		8	error code
	RXTA		8	current track
	RXSA		8	current sector
	STAPTR		3	controller state
	BUFPTR		3	buffer pointer
	INT		1	interrupt pending flag
	ERR		1	error flag (CSR<15>)
	TR		1	transfer ready flag (CSR<7>)
	IE		1	interrupt enable flag (CSR<6>)
	DONE		1	device done flag (CSR<5>)
	CTIME		24	command completion time
	STIME		24	seek time, per track
	XTIME		24	transfer ready delay
	STOP_IOE	1	stop on I/O error

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

RX01 data files are buffered in memory; therefore, end of file and OS
I/O errors cannot occur.

5.5 RL11(V12)/RL01,RL02

RL11 options include the ability to set units write enabled or write locked,
and to set the drive size to RL01, RL02, or autosize:

	SET RLn LOCKED		set unit n write locked
	SET RLn ENABLED		set unit n write enabled
	SET RLn RL01		set size to RL01
	SET RLn RL02		set size to RL02
	SET RLn AUTOSIZE	set size based on file size at attach

The size options can be used only when a unit is not attached to a file.

The RL11 implements these registers:

	name		size	comments

	RLCS		16	control/status
	RLDA		16	disk address
	RLBA		16	memory address
	RLBAE		6	memory address extension (RLV12)
	RLMP..RLMP2	16	multipurpose register queue
	INT		1	interrupt pending flag
	ERR		1	error flag (CSR<15>)
	DONE		1	device done flag (CSR<7>)
	IE		1	interrupt enable flag (CSR<6>)
	INT		1	interrupt pending flag
	STIME		24	seek time, per cylinder
	RTIME		24	rotational delay
	STOP_IOE	1	stop on I/O error

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

	end of file	x	assume rest of disk is zero

	OS I/O error	x	report error and stop

5.6 Symbolic Display and Input

The PDP-11 simulator implements symbolic display and input.  Display is
controlled by command line switches:

	-a			display as ASCII character
	-c			display as two character ASCII string
	-m			display instruction mnemonics

Input parsing is controlled by the first character typed in:

	'			ASCII character
	"			two character ASCII string
	alphabetic		instruction mnemonic
	numeric			octal number

Instruction input uses standard PDP-11 assembler syntax.  There are sixteen
instruction classes:

class		operands		examples		comments

no operands	none			HALT, RESET
3b literal	literal, 0 - 7		SPL
6b literal	literal, 0 - 077	MARK
8b literal	literal, 0 - 0377	EMT, TRAP
register	register		RTS
sop		specifier		SWAB, CLR, ASL
reg-sop		register, specifier	JSR, XOR, MUL
fop		flt specifier		ABSf, NEGf
ac-fop		flt reg, flt specifier	LDf, MULf
ac-sop		flt reg, specifier	LDEXP, STEXP
ac-moded sop	flt reg, specifier	LDCif, STCfi
dop		specifier, specifier	MOV, ADD, BIC
cond branch	address			BR, BCC, BNE
sob		register, address	SOB
cc clear	cc clear instructions	CLC, CLV, CLZ, CLN	combinable
cc set		cc set instructions	SEC, SEV, SEZ, SEN	combinable

For floating point opcodes, F and D variants, and I and L variants, may be
specified regardless of the state of FPS.

The syntax for specifiers is as follows:

syntax		specifier	displacement	comments

Rn		0n		-
Fn		0n		-		only in flt reg classes
(Rn)		1n		-
@(Rn)		7n		0		equivalent to @0(Rn)
(Rn)+		2n		-
@(Rn)+		3n              -
-(Rn)		4n              -
@-(Rn)		5n              -
{+/-}d(Rn)	6n		{+/-}d
@{+/-}d(Rn)	7n		{+/-}d
#n		27		n
@#n		37		n
.+/-n		67		+/-n - 4
@.+/-n		77		+/-n - 4
{+/-}n		67		{+/-}n - PC - 4	if on disk, 37 and n
@{+/-}n		77		{+/-}n - PC - 4	if on disk, invalid


6. Nova Features

The Nova simulator is configured as follows:

device		simulates
name(s)

CPU		Nova CPU with 32KW of memory
-		hardware multiply/divide
PTR,PTP		paper tape reader/punch
TTI,TTO		console terminal
LPT		line printer
CLK		real-time clock
DK		head-per-track disk controller
DP		moving head disk controller with four drives
MT		magnetic tape controller with eight drives

The Nova simulator implements these unique stop conditions:

	- reference to undefined I/O device, and STOP_DEV is set
	- more than INDMAX indirect addresses are detected during
	  an interrupt
	- more than INDMAX indirect addresses are detected during
	  memory reference address decoding

6.1 CPU

The only CPU options are the presense of the multiply/divide instructions
and the size of main memory.

	SET CPU MDV		enable multiply/divide
	SET CPU NOMDV		disable multiply/divide
	SET CPU 4K		set memory size = 4K
	SET CPU 8K		set memory size = 8K
	SET CPU 12K		set memory size = 12K
	SET CPU 16K		set memory size = 16K
	SET CPU 20K		set memory size = 20K
	SET CPU 24K		set memory size = 24K
	SET CPU 28K		set memory size = 28K
	SET CPU 32K		set memory size = 32K

If memory size is being reduced, and the memory being truncated contains
non-zero data, the simulator asks for confirmation.  Data in the truncated
portion of memory is lost.  Initial memory size is 32K.

CPU registers include the visible state of the processor as well as the
control registers for the interrupt system.

	name		size	comments

	PC		15	program counter
	AC0..AC3	16	accumulators 0..3
	C		1	carry
	SR		16	front panel switches
	PI		16	priority interrupt mask
	ION		1	interrupt enable
	ION_DELAY	1	interrupt enable delay for ION
	PWR		1	power fail interrupt
	INT		15	interrupt pending flags
	BUSY		15	device busy flags
	DONE		15	device done flags
	DISABLE		15	device interrupt disable flags
	STOP_DEV	1	stop on undefined IOT
	INDMAX		15	maximum number of nested indirects
	OLDPC		15	PC prior to last JMP, JMS, or interrupt
	BREAK		16	breakpoint address (177777 to disable)
	WRU		8	interrupt character

6.2 Programmed I/O Devices (PTR, PTP, TTI, TTO, CLK, LPT)

The paper tape reader (PTR), paper tape punch (PTP), and line printer
(LPT) read data from or write data to disk files.  The POS register
specifies the number of the next data item to be read or written.  Thus,
by changing POS, the user can backspace or advance these devices.

The programmed I/O devices typically implement these registers:

	name		size	comments

	BUF		8	last data item processed
	BUSY		1	device busy flag
	DONE		1	device done flag
	DISABLE		1	interrupt disable flag
	INT		1	interrupt pending flag
	TIME		24	time from I/O initiation to interrupt
				(for keyboard, polling interval)
	POS		32	position in the input or output file
	STOP_IOE	1	stop on I/O error

For the serial devices, error handling is as follows:

	type	error	     STOP_IOE	processed as

	in,out	not attached	1	report error and stop
				0	out of tape or paper

	in	end of file	1	report error and stop
				0	out of tape or paper

	in,out	OS I/O error	x	report error and stop

Terminal options include the ability to set limited Dasher compatibility
mode or normal mode:

	SET TTI ANSI		normal mode
	SET TTI DASHER		Dasher mode
	SET TTO ANSI		normal mode
	SET TTO DASHER		Dasher mode

Setting either TTI or TTO changes both devices.  In Dasher mode, carriage
return is changed to newline on input, and ^X is changed to backspace.

6.3 Fixed Head Disk (DK)

The fixed head disk controller implements these registers:

	name		size	comments

	STAT		16	status
	DA		16	disk address
	MA		16	memory address
	BUSY		1	device busy flag
	DONE		1	device done flag
	DISABLE		1	device disable flag
	INT		1	interrupt pending flag
	WLK		8	write lock switches
	TIME		24	rotational delay, per sector
	STOP_IOE	1	stop on I/O error

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

Fixed head disk data files are buffered in memory; therefore, end of file
and OS I/O errors cannot occur.

6.4 Moving Head Disk (DP)

Moving head disk options include the ability to place units online or
offline, write enabled or write locked, and to select the type of drive:

	SET DPn OFFLINE		set unit n offline
	SET DPn ONLINE		set unit n online
	SET DPn LOCKED		set unit n write locked
	SET DPn ENABLED		set unit n write enabled
	SET DPn FLOPPY		set unit n to floppy disk
	SET DPn D31		set unit n to Diablo 31
	SET DPn D44		set unit n to Diablo 44
	SET DPn C111		set unit n to Century 111
	SET DPn C114		set unit n to Century 114

All drives have 256 16b words per sector.  The other disk parameters are:

	drive cylinders surfaces sectors size (MW) 	DG models

	floppy	77	1	8	  .158		6038
	D31	203	2	12	 1.247		4047, 4237, 4238
	D44	408	4	12	 5.014		4234, 6045
	C111	203	10	6	 3.118		4048
	C114	203	20	12	12.472		4057, 2314

The moving head disk controller implements these registers:

	name		size	comments

	FCCY		16	flags, command, cylinder
	USSC		16	unit, surface, sector, count
	STAT		16	status
	MA		16	memory address
	BUSY		1	device busy flag
	DONE		1	device done flag
	DISABLE		1	interrupt disable flag
	INT		1	interrupt pending flag
	STIME		24	seek time, per cylinder
	RTIME		24	rotational delay

Error handling is as follows:

	error		processed as

	not attached	disk not ready

	end of file	assume rest of disk is zero

	OS I/O error	report error and stop

6.5 Magnetic Tape (MT)

Magnetic tape options include the ability to place units write enabled or
or write locked.

	SET MTn LOCKED		set unit n write locked
	SET MTn ENABLED		set unit n write enabled

The magnetic tape controller implements these registers:

	name		size	comments

	CU		16	command, unit
	MA		16	memory address
	WC		16	word count
	STA1		16	status word 1
	STA2		16	status word 2
	EP		1	extended polling mode (not supported)
	BUSY		1	device busy flag
	DONE		1	device done flag
	DISABLE		1	interrupt disable flag
	INT		1	interrupt pending flag
	STOP_IOE	1	stop on I/O error
	CTIME		24	controller delay
	RTIME		24	record delay
	UST0..7		32	unit status, units 0..n

Error handling is as follows:

	error		processed as

	not attached	tape not ready

	end of file	(read or space) end of physical tape
			(write) ignored

	OS I/O error	report error and stop

6.6 Symbolic Display and Input

The Nova simulator implements symbolic display and input.  Display is
controlled by command line switches:

	-a			display as ASCII character
	-c			display as two character ASCII string
	-m			display instruction mnemonics

Input parsing is controlled by the first character typed in:

	'			ASCII character
	"			two character ASCII string
	alphabetic		instruction mnemonic
	numeric			octal number

Instruction input uses standard Nova assembler syntax.  There are three
instruction classes: memory reference, IOT, and operate.

Memory reference instructions have the format

	memref {ac,}{@}address{,index}

LDA and STA require an initial register; ISZ, DSZ, JSR, and JMP do not.
The syntax for addresses and indices is as follows:

syntax		mode	displacement	comments

0 <= n < 0400	0	n
{+/-}n >= 0400	1	{+/-}n - PC	must be in range [-200, 177]
					invalid on disk
.+/-n		1	{+/-}n		must be in range [-200, 177]
{+/-}n,2	2	{+/-}n		must be in range [-200, 177]
{+/-}n,3	3	{+/-}n		must be in range [-200, 177]

IOT instructions have one of four formats

	syntax			example

	iot			HALT
	iot reg			INTA
	iot device		SKPDN
	iot reg,device		DOAS

Devices may be specified as mnemonics or as numbers in the range 0 - 077.

Operate instructions have the format

	opcode{#} reg,reg{,skip}

In all Nova instructions, blanks may be substituted for commas as field
delimiters.


7. 18b PDP Features

The four 18b PDP's (PDP-4, PDP-7, PDP-9, PDP-15) are very similar and
are configured as follows:

system	device		simulates
	name(s)

PDP-4	CPU		PDP-4 CPU with 8KW of memory
	PTR,PTP		integral paper tape/Type 75 punch
	TTI,TTO		KSR28 console terminal (Baudot code)
	LPT		Type 62 line printer (Hollerith code)
	CLK		integral real-time clock

PDP-7	CPU		PDP-7 CPU with 32KW of memory
	-		Type 177 extended arithmetic element (EAE)
	-		Type 148 memory extension
	PTR,PTP		Type 444 paper tape reader/Type 75 punch
	TTI,TTO		KSR 33 console terminal
	LPT		Type 647 line printer
	CLK		integral real-time clock
	DRM		Type 24 serial drum

PDP-9	CPU		PDP-9 CPU with 32KW of memory
	-		KE09A extended arithmetic element (EAE)
	-		KG09B memory extension
	-		KP09A power detection
	-		KX09A memory protection
	PTR,PTP		PC09A paper tape reader/punch
	TTI,TTO		KSR 33 console terminal
	LPT		Type 647E line printer
	CLK		integral real-time clock
	RF		RF09/RS09 fixed-head disk
	MT		TC59/TU10 magnetic tape

PDP-15	CPU		PDP-15 CPU with 32KW of memory
	-		KE15 extended arithmetic element (EAE)
	-		KF15 power detection
	-		KM15 memory protection
	PTR,PTP		PC15 paper tape reader/punch
	TTI,TTO		KSR 35 console terminal
	LPT		LP15 line printer
	CLK		integral real-time clock
	RP		RP15/RP02 disk pack
	RF		RF15/RS09 fixed-head disk
	MT		TC59/TU10 magnetic tape

The 18b PDP simulators implement one unique stop condition: if an undefined
instruction (unimplemented OPR) is decoded, and register STOP_INST is set,
the simulator halts.

7.1 CPU

The only CPU options are the presense of the EAE and the size of main memory.

	SET CPU EAE		enable EAE
	SET CPU NOEAE		disable EAE
	SET CPU 4K		set memory size = 4K
	SET CPU 8K		set memory size = 8K
	SET CPU 12K		set memory size = 12K
	SET CPU 16K		set memory size = 16K
	SET CPU 20K		set memory size = 20K
	SET CPU 24K		set memory size = 24K
	SET CPU 28K		set memory size = 28K
	SET CPU 32K		set memory size = 32K
	SET CPU 48K		set memory size = 48K
	SET CPU 64K		set memory size = 64K
	SET CPU 80K		set memory size = 80K
	SET CPU 96K		set memory size = 96K
	SET CPU 112K		set memory size = 112K
	SET CPU 128K		set memory size = 128K

Memory sizes greater than 8K are only available on the PDP-7, PDP-9, and
PDP-15; memory sizes greater than 32KW are only available on the PDP-15.
If memory size is being reduced, and the memory being truncated contains
non-zero data, the simulator asks for confirmation.  Data in the truncated
portion of memory is lost.  Initial memory size is 8K for the PDP-4, 32K
for the PDP-7 and PDP-9, and 128K for the PDP-15.

CPU registers include the visible state of the processor as well as the
control registers for the interrupt system.

	system	name		size	comments

	all	PC		addr	program counter
	7,9	PC		15	program counter
	15	PC		17	program counter
	all	AC		18	accumulator
	7,9,15	MQ		18	multiplier-quotient
	7,9,15	SC		6	shift counter
	7,9,15	EAE_AC_SIGN	1	EAE AC sign
	all	L		1	link
	7,9	EXTM		1	extend mode
	15	BANKM		1	bank mode
	7	TRAPM		1	trap mode
	9,15	USMD		1	user mode
	9,15	USMDBUF		1	user mode buffer
	9,15	BR		addr	memory protection bounds
	7,9,15	TRAPP		1	trap pending
	9,15	NEXM		1	non-existent memory violation
	9,15	PRVN		1	privilege violation
	7,9	EMIRP		1	EMIR instruction pending
	9,15	RESTP		1	DBR or RES instruction pending
	15	XR		18	index register
	15	LR		18	limit register
	all	SR		18	front panel switches
	all	INT		32	interrupt requests
	all	IORS		18	IORS register
	all	ION		1	interrupt enable
	all	ION_DELAY	2	interrupt enable delay
	all	OLDPC		addr	PC prior to last transfer
	all	STOP_INST	1	stop on undefined instruction
	all	BREAK		18	breakpoint address (177777 to disable)
	all	WRU		8	interrupt character

"addr" signifies the address width of the system (13b for the PDP-4, 15b for
the PDP-7 and PDP-9, 17b for the PDP-15).

7.2 Programmed I/O Devices (PTR, PTP, TTI, TTO, CLK, LPT)

The paper tape reader (PTR), paper tape punch (PTP), and line printer
(LPT) read data from or write data to disk files.  The POS register
specifies the number of the next data item to be read or written.  Thus,
by changing POS, the user can backspace or advance these devices.

The programmed I/O devices typically implement these registers:

	name		size	comments

	BUF		8	last data item processed
	INT		1	interrupt pending flag
	DONE		1	device done flag
	TIME		24	time from I/O initiation to interrupt
				(for keyboard, polling interval)
	POS		32	position in the input or output file
	STOP_IOE	1	stop on I/O error

For the serial devices, error handling is as follows:

	type	error	     STOP_IOE	processed as

	in,out	not attached	1	report error and stop
				0	out of tape or paper

	in	end of file	1	report error and stop
				0	out of tape or paper

	in,out	OS I/O error	x	report error and stop

7.3 RP15/RP02

RP15 options include the ability to place units write enabled or
write locked:

	SET RPn LOCKED		set unit n write locked
	SET RPn ENABLED		set unit n write enabled

The RP15 implements these registers:

	name		size	comments

	STA		18	status A
	STB		18	status B
	DA		18	disk address
	MA		18	current memory address
	WC		18	word count
	INT		1	interrupt pending flag
	BUSY		1	control busy flag
	STIME		24	seek time, per cylinder
	RTIME		24	rotational delay
	STOP_IOE	1	stop on I/O error

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

	end of file	x	assume rest of disk is zero

	OS I/O error	x	report error and stop

7.4 DRM

The drum has no options.  It implements these registers:

	name		size	comments

	DA		9	drum address (sector number)
	MA		15	current memory address
	INT		1	interrupt pending flag
	DONE		1	device done flag
	ERR		1	error flag
	WLK		32	write lock switches
	TIME		24	rotational latency, per word
	STOP_IOE	1	stop on I/O error

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

Drum data files are buffered in memory; therefore, end of file and OS
I/O errors cannot occur.

7.5 RF09/RF15/RS09

The RF09/RF15 implements these registers:

	name		size	comments

	STA		18	status
	DA		21	current disk address
	MA		18	memory address (in memory)
	WC		18	word count (in memory)
	BUF		18	data buffer (diagnostic only)
	INT		1	interrupt pending flag
	WLK0..7		16	write lock switches for disks 0..7
	TIME		24	rotational delay, per word
	BURST		1	burst flag
	STOP_IOE	1	stop on I/O error

The RF15/RF09 is a three-cycle data break device.  If BURST = 0, word
transfers are scheduled individually; if BURST = 1, the entire transfer
occurs in a single data break.

Error handling is as follows:

	error	     STOP_IOE	processed as

	not attached	1	report error and stop
			0	disk not ready

RF15/RF09 data files are buffered in memory; therefore, end of file and OS
I/O errors cannot occur.

7.6 Magnetic Tape (MT)

Magnetic tape options include the ability to place units write enabled or
or write locked.

	SET MTn LOCKED		set unit n write locked
	SET MTn ENABLED		set unit n write enabled

The magnetic tape controller implements these registers:

	name		size	comments

	CMD		18	command
	STA		18	main status
	MA		18	memory address (in memory)
	WC		18	word count (in memory)
	INT		1	interrupt pending flag
	STOP_IOE	1	stop on I/O error
	TIME		24	record delay
	UST0..7		24	unit status, units 0..n

Error handling is as follows:

	error		processed as

	not attached	tape not ready

	end of file	(read or space) end of physical tape
			(write) ignored

	OS I/O error	report error and stop

7.7 Symbolic Display and Input

The 18b PDP simulators implement symbolic display and input.  Display is
controlled by command line switches:

	-a			display as ASCII character
	-c			display as (sixbit) character string
	-m			display instruction mnemonics

The PDP-15 also recognizes an additional switch:

	-p			display as packed ASCII (five 7b ASCII
				characters in two 18b words)

Input parsing is controlled by the first character typed in:

	'			ASCII character
	"			three character sixbit string
	alphabetic		instruction mnemonic
	numeric			octal number

The PDP-15 also recognizes an additional input mode:

	#			five character packed ASCII string in
				two 18b words

Instruction input uses standard 18b PDP assembler syntax.  There are six
instruction classes: memory reference, EAE, index (PDP-15 only), IOT,
operate, and LAW.

Memory reference instructions have the format

	memref {I/@} address{,X}

where I (PDP-4, PDP-7, PDP-9) /@ (PDP-15) signifies indirect reference,
and X signifies indexing (PDP-15 in page mode only).  The address is an
octal number in the range 0 - 017777 (PDP-4, PDP-7, PDP-9, and PDP-15 in
bank mode) or 0 - 07777 (PDP-15 in page mode).

IOT instructions consist of single mnemonics, eg, KRB, TLS.  IOT instructions
may be or'd together

	iot iot iot...

IOT's may also include the number 10, signifying clear the accumulator

	iot 10

The simulator does not check the legality of IOT combinations.  IOT's for
which there is no opcode may be specified as IOT n, where n is an octal
number in the range 0 - 07777.

EAE instructions have the format

	eae {+/- shift count}

EAE instructions may be or'd together

	eae eae eae...

The simulator does not check the legaility of EAE combinations.  EAE's for
which there is no opcode may be specified as EAE n, where n is an octal
number in the range 0 - 037777.

Index instructions (PDP-15 only) have the format

	index {immediate}

The immediate, if allowed, must be in the range of -0400 to +0377.

Operate instructions have the format

	opr opr opr...

The simulator does not check the legality of the proposed combination.  The
operands for MUY and DVI must be deposited explicitly.

Finally, the LAW instruction has the format

	LAW immediate

where immediate is in the range of 0 to 017777.


Appendix 1: Notes On File Representations

1. Disks

Disks are represented as unstructured binary files of 16b data items.  Thus,
simulated disks are endian dependent.  To share a disk file between versions
of the simulator running on big and little endian systems, each 16b word
must be byte swapped prior to use.

2. Magnetic tapes

Magnetic tapes are represented as unstructured binary files of 16b data
items.  Each record consists of a 16b byte count n, followed by (n + 1)/2
16b words of data.  If the byte count is odd, the last byte in the record
is undefined.

Magnetic tapes are endian dependent.  To share a magnetic tape file between
versions of the simulator running on big and little endian systems, each
16b word must be byte swapped prior to use.

Note that the representation of magnetic tapes is only consistent within
each simulator family.  On a little endian system, a magnetic tape produced
by the Nova simulator will appear to be "correct" for the PDP-11 simulator,
even though on real hardware the results would be byte swapped.  Interchange
of tapes between simulators is not supported.


Revision History (since Rev 1.1)

Rev 2.2 Jan, 96	Added register buffers for save/restore
		Added 18b PDP's
		Guaranteed TTI, CLK times are non-zero
		Fixed breakpoint/RUN interaction bug
		Fixed magnetic tape backspace to EOF bug
		Fixed ISZ/DCA inversion in PDP-8 symbol table
		Fixed sixbit conversion in PDP-8 examine/deposit
		Fixed unit number calculation bug in SCP and in
			Nova, PDP-11, 18b PDP moving head disks

Rev 2.1	Dec, 95	Fixed PTR bug (setting done on EOF) in PDP-8, Nova
		Fixed RX bug (setting error on INIT if drive 1 is
			not attached) in PDP-8, PDP-11
		Fixed RF treatment of photocell flag in PDP-8
		Fixed autosize bug (always chose smallest disk if new
			file) in PDP-11, Nova
		Fixed not attached bug (reported as not attachable) in
			most mass storage devices
		Fixed Nova boot ROMs
		Fixed bug in RESTORE (didn't requeue if delay = 0)
		Fixed bug in RESTORE (clobbered device position)
		Declared static constant arrays as static const
		Added PDP-8, Nova magnetic tape simulators
		Added Dasher mode to Nova terminal simulator
		Added LINUX support

Rev 2.0	May, 95	Added symbolic assembly/disassembly